Gluex Detector Tasks/Status

Solenoid

- Coil repairs contract complete

- Support structure– need to tie in with BCAL, George/Floyd working

- Need to tie in with Target cryogenic system

- Leak testing showed all in house coils are leak tight

- George/Floyd revisiting magnetic field with ANSYS, developing baseline, adding cladding

Target

- Slava is starting to work on Target, Met with M. Seely, S. Christo

- Need to meet with Mike Seely to develop design

- 2 cm diameter selected for target

- Shortened Target cart to fit CDC on upstream platform

- PLC’s to be used for control

- Probably incorporate buffer dewar or possibly separate refrig.

- Need to develop operating requirements

- Need to sit w/D. Kashey to discuss design particulars

- 2cm dia kapton target

Start Counter

- Werner put out geometry specification

- Chuck working to develop mechanical design

- 40 channels

- 6.5 cm radius

- Spiral design to eliminate cracks in particle detection

- Look at fine mesh Hamamatsu PMT’s

CDC

- Mostly done in design (preliminary)

- Mechanical prototype being built

- Electronic mounting and gas system need more work

- Possibility of mixing some methane

- Need to hash out LV distr. Box location

- Need to look at downstream wire supports to reduce material

BCAL

- Need to complete insertion design

- Alberta say machinability of wedges ok

- Need to revise base plate for prototype machining

- Need to visit Alberta to nail dowm mechanical details

- Layup and machining going to take place in Alberta

- Use of 8mm aluminum plate decided upon for inside surface

- Look at ways to make light tight

- Look at ways to mount SiPM’s

- Look at alternative designs for inner area of wedge

FDC

- Latest cooling scheme (24 circuits total with florinert) looks to be acceptable

- Cooling prototype made and awaiting test

- Produce prototype baseline drawings – first cut almost done- if all is well, these will be the production dwgs also

- Cathode flatness test showed problems, need to address cathode flatness

TOF

- Developed concept for connecting to FCAL

- Developed (with Matt Sheppard) support structure concept

- Initial PMT structure concept ok depending on magnetic fields

- Phototube housing needs to be at neg. HV

FCAL

- Need to revisit lead glass frame

- Temperature test of cockroft-walton showed no significant temp increase with plastic cell wall

- Cookie compression test showed 2 psi initial, then maybe 1 psi to hold in place

- Design support structure with rails (preliminary).

- Add dark room with cooling (preliminary)

- George to rerun magnetic shielding analysis

- Look into doing a mag field test on 8x8 array

- 64 cell prototype being built at IU

- “Primex” style prototype built.

Tagger

- Jim looking in to all aspects

- Designer (Brent) to work to bring to 60%

- PED contract cancelled, will do design/build under construction

- SOW and Spec written and being reviewed by Jim

- Interface dwg preliminary done

Hodoscope

- Have initial assy dwg from Richard and Franz

- Franz to do design

- Must mount on Tagger stand

Microoscope

- Have initial assy dwg

- Richar/Franz to complete design

Collimator

- Have initial assy dwg and some details

- James making 3D model of active collimator (complete)

- Working with Richard to iron out locations, initial layout complete, to be worked out with Sasha’s MC analysis

Pair Spectrometer

- Have initial assy dwg from Hall B

- YERPHI to write spec.

- Need to develop layout for possible locations

Radiator

- Look at Goniometer from German company

- New support for thin radiator to be designed

Infrastructure

- Bill and James to Develop Platforms designs

- Initial cable routing scheme developed, more work needed

- Perform global cooling analysis

- Updated rack quantities and positions

- Gas systems details to be worked out

- May review went well!