Gluex Detector Tasks/Status

Solenoid

- Coil repairs contract complete

- Upstream ring in process of getting machined

- Designer needed ½ time to work on cryogenics and structure

- Support structure– need to tie in with BCAL

- Need to tie in with Target cryogenic system

- ½ time designer started February

- Leak testing underway

- George revisiting magnetic field with ANSYS

UPV

- On hold

Target

- Action tracker updated to reflect geometry questions for target

- Met with Mike Seely and determined input for tracker

- 2 cm diameter selected

- Need to shorten Target cart to fit CDC on upstream platform

- PLC’s to be used for control

- Probably incorporate buffer dewar

- Need to develop operating requirements

Start Counter

- Werner put out geometry specification soon

- 40 channels

- 6.5 cm radius

CDC

- Hazard Analysis sheet done

- IGUS rails/bearings selected for FDC/CDC rails

- CMU received feedthru to test

- Preliminary Design for insertion tooling complete (same as FDC)

- Developed alignment scheme and features (all permanent features must be non-magnetic)

- Slava/James have developed design

- Possibility of mixing some ethane, need to review ES$H manual

BCAL

- Review and update current insertion concept

- Regina looking at machinability of wedges

- Scale model made by Florida

- Design assy/installation cart (preliminary done)

- Layup and machining going to take place in Alberta

- Use of 6mm aluminum plate decided upon for inside surface

FDC

- Latest cooling scheme (24 circuits total with florinert) looks to be acceptable

- Include cooling scheme on prototype

- Produce prototype baseline drawings – first cut almost done- if all is well, these will be the production dwgs also

- Deflection test on wireframe successful

- IGUS rails/bearings selected for FDC/CDC rails

- Strong back design developed

- Installation tooling developed (preliminary)

- 55 shore A durometer viton selected for o-ring

Cerenkov

- On hold

TOF

- Developed concept for connecting to FCAL

- Developed (with Matt Sheppard) support structure concept

FCAL

- Need to revisit lead glass frame

- Temperature test of cockroft-walton showed no significant temp increase with plastic cell wall

- Cookie compression test showed 2 psi initial, then maybe 1 psi to hold in place

- Design support structure with rails (preliminary).

- Add dark room with cooling (preliminary)

- George to rerun magnetic shielding analysis

- Look into doing a mag field test on 8x8 array

- 64 cell prototype being built at IU

- Light guide test good

Tagger

- Need to double check the Protvino vs. Autocad model

- PED contract cancelled, will do design/build under construction

- ½ designer needed to bring design to 60%

- SOW and Spec written

- Interface dwg in work (discrepancy with civil)

Hodoscope

- Have initial assy dwg from Richard and Franz

Microoscope

- Have initial assy dwg

Collimator

- Have initial assy dwg and some details

Pair Spectrometer

- Have initial assy dwg from Hall B

- YERPHI to write spec.

Radiator

- Look at Goniometer from German company

- New support for thin radiator to be designed

Infrastructure

- Develop Platforms designs  (Front, Rear, Side)

- Develop cable routing scheme, work with elecrical

- Perform global cooling analysis

- Need to Update rack quantities and positions

- Gas systems

- Developing complete system for May review