CDC assembly procedure                                                          5-01-2009

- Lay endplates on a flat layout table and glue in the inner window supports.

- Install fixed flange onto stringing pipe fixture in horizontal position.

- Slide upstream endplate onto fixed flange.

- Slide inner gas window tube onto pipe and glue to upstream endplate window support.

- Install downstream endplate onto sliding pipe flange.

- Slide endplate/flange assembly onto stringing pipe and insert downstream window support into window tube.

- Loosely assemble 12 permanent outside and 12?  temporary inside endplate connecting rods.

- Tighten 24 rods to upstream endplate.

- Tighten downstream endplate to 24 connecting rods in a criss-cross pattern, possibly using alternating right hand and left hand threads to reduce torque on endplate.

- Tighten sliding flange to pipe.

- Rotationally align endplates with transit and glue downstream gas window tube.

- Install turnbuckle rods from top of pipe to ends of 12 permanent outside downstream connecting rods to support circumference of endplates.

- Crane detector/pipe assembly to vertical position.

- Glue feedthroughs thru endplates into pre-made straw tubes/doughnuts, gluing straw tubes together lengthwise as you go.

- Glue outside gas window supports and gas window.

- String wires to 30 grams tension.

- Rotate chamber to horizontal position and support endplates on bearing blocks.

- Install plexi-glass wire position plate and downstream gas plenum.

- Wire all connectors.

- Rotate vertically and glue all wire feedthroughs in wire position plate.

- Run argon/ethane gas mix and check for leaks and reseal as necessary.