## Slide 1: Recent Progress on Controls
Elliott Wolin
Hall D Online Meeting
4-Mar-2009

## Slide 2: Motivation
A few weeks ago Elke asked how long it would take to get an EPICS system going
I didn’t know
  I had never installed EPICS
  I knew nothing about the framework or make system
  I knew next to nothing about EPICS databases
  Only had used some utilities and libs previously
  But I did understand basic idea of EPICS
She also said she’d like to see a test controls system running

## Slide 3: Progress Report
I downloaded EPICS base and some extensions
I figured out how to use the make system
I installed missing system libraries (via rpm)
I compiled and linked base and extensions
I successfully ran utilities and test programs
This took two or three days spread out over a little less than a week

## Slide 4: More Progress
I developed a custom app using “sub” records
  I supplied init() and process() functions
  EPICS framework took care of everything else
  I implemented a fake device (sawtooth function)
I successfully ran app, ALH, and striptool
I ran Accelerator archiver and viewer
  On Accelerator computer
This took three or four days spread out over a week

## Slide 5: Upshot
It took about five days of effort spread out over two weeks to install from scratch, run tests, then develop a custom app that included alarming, stripcharts, and archiving/viewing
It has been running continuously for about three weeks now, no problems

## Slide 6: Comments
The alarm system, strip chart tool, and archiver are likely NOT the ones we will use in Hall D
More powerful versions are under development, especially at the SNS
I will test them as they become available

## Slide 7: Other Work
“sub” records on Linux require linking functions into the executable
Need separate executable for every db file
I.e. dynamic linking is not supported
With advice from an ANL EPICS guru I developed a way to get functions from dll (no linking needed)
  new iocShell command registerDLFunctions() scans dll symbol table and registers relevant functions
  functions now available to INAM and SNAM specifications used by “sub” records in db files
  guru will implement something similar in next EPICS release

## Slide 8: iocShell Startup Commands
## load functions from shared library
registerDLFunctions libdlExample.so
Functions reside in .so file
Functions must be marked via special macro
Libraries needed by functions must be included
Must set LD_LIBRARY_PATH appropriately

## Slide 9: db File
record(sub,”dlExample1") {
field(INAM,"dlInit1")
field(SNAM,"dlProc1")
field(SCAN,"1 second")
}
Creates EPICS PV dlExample1
Calls dlInit1() once
Calls dlProc1() to process record
dlInit1() and dlProc1() reside in .so file

## Slide 10: Labview
JLab has Labview site license
  Labview runs on Linux, Windows
  Virtual Instruments machine independent (but…)
What role might Labview play in Hall D
  already used for bench test systems
  production uses are in SCADA layer (not DCS)
    expert gui’s, e.g. CAEN mainframe, Wiener crate?
    operator gui’s, adjunct to CSS or replace?
What if site license disappears?
I will soon test Labview on Linux
  CAEN mainframe
I will check recent conference proceedings

## Slide 11: Near-Term Plans
Continue learning about EPICS
Connect EPICS to real devices
  PLC
  CAEN mainframe
Test EPICS utilities as they become available
Attend EPICS collaboration meetings and ICALEPCS conferences
Test Linux Labview with real devices
Find out about Labview use in production HENP experiments (met w/sales reps on Tues)
Should I create a mini-EPICS dist? For test setups?

## Slide 12: DEMO